## Slide 1
Anthony Steed

## Slide 2: Part 1: Introduction Networking Fundamentals
Anthony Steed

## Slide 3: Goals
Understanding the application domain
Understanding the constraints the theoretical and practical constraints of distributed simulation over the Internet
Common strategies for mitigating constraints whilst satisfying
Practical tools for building networked virtual environments and networked games
Examples and literature that you can use to further your own knowledge

## Slide 4: Session 1 (9:00 – 10:30)
Introduction
- What are networked graphics?
- Potted history of networked graphics
Networking Fundamentals
- Basic Internet technologies
- Basic networking strategies
- Why are all types of networked graphics “non-standard” networking applications?

## Slide 5: Session 2 (11:00 –12:30)
Actual Internet Performance
- What bandwidth can we expect?
- Sources of latency
- What other issues must we consider?
Requirements and Constraints
- Requirements on consistency
- Requirements on latency
- User response to inconsistency and latency

## Slide 6: Session 3 (13.30 – 15:00)
Latency
- Mitigation strategies
- Playout delays, local lag and dead reckoning
Scalability
- Management of awareness
- Interest specification
- Server partitioning

## Slide 7: Session 4 (15:15 – 16:45)
Application Support
- Security, Protocol decisions
- Persistence
Tools
- Middleware
- Networked engines
Research Issues
- Scalable peer-to-peer, thin clients
- Standards, etc.

## Slide 8: Materials
See handout
All materials available from speaker
Also on:
  http://www.networkedgraphics.org/materials/ieeevr-2011
Many more materials (code, blog posts, paper links, etc.) on:
  http://www.networkedgraphics.org/

## Slide 9: For Much More Detail
Anthony Steed & Manuel Oliveira
Published by Morgan Kaufmann (2009 US, 2010 EU&Other)
576 pages
Covers today’s topics in more depth plus more background

## Slide 10: Introduction
Anthony Steed

## Slide 11: Introduction
What are networked graphics?
Potted history of networked graphics

## Slide 12: WHAT ARE NVES AND NGS?

## Slide 13: DIVE

## Slide 14: Second Life
Notes: IEEE Virtual Reality 2009 programme committee meeting, autumn 2008

## Slide 15: Burnout™ Paradise

## Slide 16: Common Themes
3D virtual environment
Real-time changes
Collaboration with other users
  Representation of users in the world (typically as avatars, but also cars/tanks/etc.)
  Text communication
  Voice
Virtual environment might mirror a real place but typically is a fantastic place

## Slide 17: Common Themes
One client is usually responsible for generating the view for one user
A set of clients creates the illusion of a shared virtual environment
“Illusion” because
  Virtual environments can involve detailed models
  Information about changes in models takes time to travel across communication links

## Slide 18: Virtual Environment Client
Notes: Figure 1.27

## Slide 19: Networked Virtual Environment
Notes: Figure 1.2

## Slide 20: Consistency and Plausibility
Local plausibility is the appearance of consistency of only local actions
Shared plausibility is the appearance of properties being the same as observed by users
  Objects that are in the background need not be consistent
  Further: only things that might be the focus of joint attention can be discussed and be different
A local implausibility might be an obvious thing to talk about!

## Slide 21: Why NVEs are not Standard Network Applications
Unlike video/audio streaming, or web browsing, in an NVE or NG client, networking is NOT the main activity: rendering probably is
Some information changes very quickly and smoothly
  E.G. player positions
Can incorporate other web-enabled media
  Audio/video
Often require bulk download of assets

## Slide 22: SOME HISTORY

## Slide 23
Simulation
Real-Time Strategy
Electronic Games
Network
Networked Games
Social Environments
MUD
E-mail
WWW
MORPGs
Notes: Figure 1.3

## Slide 24: ARPANET
Diagram of ARPANET circa 1977

## Slide 25: SIMNET
SIMNET aircraft simulation. Left: A view of the simulator control. Right: a view from the cockpit of an aircraft simulator. Images from ( Harris, 1994)

## Slide 26: MUD1
A screenshot of the text interface of the MUD1 system over a standard telnet client

## Slide 27: Maze (Maze War)
Maze War running at on Imlac PSD-1D at DigiBarn's Maze War 30 Year Retrospective (Digibarn, 2004)

## Slide 28: BZFlag
A screenshot of the current BZFlag

## Slide 29: DOOM
DOOM™ (iD Software) was the first multi-player first-person shooter to reach wide-spread public attention

## Slide 30: Quake
Quake (id Software) brought true 3D and was the basis for several licensed games. Left: the original Quake game. Right: Counter-Strike (Valve Software), originally a modification of the game Half-Life which was based on Quake engine.

## Slide 31: Meridian 59
Meridian 59. Left: a view of the client. Right: an army of skeletons invades the Streets of Tos. This screenshot is from a more recent version of the client software.

## Slide 32: Ultima Online
Pirates demanding tribute
(Schultz, A., 2009)

## Slide 33: Active Worlds
Left: Map of Alphaworld in December 1996. Right: Map of Alphaworld in August 2001.

## Slide 34: Networking Fundamentals
Anthony Steed

## Slide 35: Networking Fundamentals
Basic Internet technologies
Basic networking strategies
Why are all types of networked graphics “non-standard” networking applications?

## Slide 36: Basic Internet Technologies

## Slide 37: Introduction
Networks at the heart of networked VR
Many network protocols are out there
  TCP, UDP, multicast, RTP, etc
  Choice based on needs
Properties of the Internet

## Slide 38: IP Stack
Application
Transport
Network
Link
Physical
DHCP, DIS, DNS, FTP, HTTP, IMAP, RTP, SMTP, SSH, Telnet
TCP, UDP, RSVP
IP, ICMP, IGMP
Ethernet, 802.11, ADSL
copper wires, fibre-optic cable, radio waves

## Slide 39: From Messages to Frames
Message
Segment
Packet
Frame
Application Data
Transport
Header
Network
Header
Link
Header
Link Footer
Application
Transport
Network
Link
Physical
Notes: Figure 3.2

## Slide 40: Application Layer

## Slide 41: Application Layer Protocols
Determine what messages are sent between applications
  Messages defined by syntax and semantics
Various standards for messages, typically set by RFCs (Requests for Comments) hosted by the IETF (Internet Engineering Task Force)

## Slide 42: E.G. HTTP Request
If you connect to Host www.cs.ucl.ac.uk at Port 80
And then issue (type!) in ASCII the following message:
      GET /staff/A.Steed/ HTTP/1.1
      Host: www.cs.ucl.ac.uk
And issues (type) two carriage returns
You get …

## Slide 43: …
HTTP/1.0 200 Document follows
MIME-Version: 1.0
Server: CERN/3.0
Date: Sun, 08 Feb 2009 15:25:18 GMT
Content-Type: text/html
Content-Length: 16150
Last-Modified: Wed, 21 Jan 2009 17:42:00 GMT
<?xml version="1.0" encoding="iso-8859-1"?>
<!DOCTYPE html PUBLIC "-//W3C//DTD XHTML 1.0 Transitional//EN" "http://www.w3.org/TR/xhtml1/DTD/xhtml1-transitional.dtd">
<html xmlns="http://www.w3.org/1999/xhtml" lang="en" dir="ltr">
<head>
<meta http-equiv="Content-Type" content="text/html; charset=iso-8859-1" />
<meta name="keywords" content="A. Steed, Anthony Steed, Department of Computer Science, University College London, virtual environments, virtual reality, computer graphics" />

## Slide 44: Application Protocol Descriptions
Often ASCII preamble with binary assets inserted at known or marked positions
Some messages are designed to be carried over a reliable stream and are of unknown length (likely to be over TCP)
Some messages are small and it is not important if they get lost (likely to be over UDP)

## Slide 45: Common Application Protocols

## Slide 46: Domain Name Service (DNS)
Maps fully qualified domain names (narok.cs.ucl.ac.uk) to their IP addresses (128.16.5.123)
Is a network service, thus takes time
Time is variable because it’s a hierarchical search
Local DNS caches query responses for a time (e.g. 24 hours)
Otherwise needs to query a canonical domain

## Slide 47: TRANSPORT LAYER

## Slide 48: Transport Layer Protocols
User Datagram Protocol (UDP)
  Send a message (datagram) and forget about it
  No guaranteed delivery
  No guaranteed ordering
Transmission Control Protocol (TCP)
  Guaranteed, in-order stream of data from one host to another

## Slide 49: End to End Principle
  Only the sender and receiver understand TCP or UDP (or other same or higher-level protocols). The other routers in the Internet do not.

## Slide 50: UDP
All hosts on the Internet have an IP address
How does the network know which program wants it?
You additionally need (for UDP and TCP) a port number
  These are 16 bits numbers, so must lie in the range 0-65535
  Some are reserved, see later
Processes listen for incoming UDP packets
Need to check the packet for consistency

## Slide 51: UDP Segment Layout
Bits | 0 15 | 16 31
0-31 | Source Port | Destination Port
32-63 | Length | Checksum
64+ | Data | 
Notes: Figure 3.4

## Slide 52
Transport
Network
Link
Transport
Network
Link
Application
Application
Application
Source Port = Port1
Destination Port = Port2
Destination Port = Port3
Notes: Figure 3.5

## Slide 53: TCP
In comparison to UDP, TCP offers:
  A connection-oriented services with bi-directional (full-duplex) communication
  Reliable transmission of messages in each direction
  Congestion avoidance, using variable rate transmission
  In order, and non-duplicate delivery of information
Applications add messages to an outgoing buffer
The buffer is streamed in packets to the receiver
The receiver reconstructs the buffer and extract packets

## Slide 54
Transport
Network
Link
Application
Msg i
Msg i-2
Msg i-1
…
Data
Header
Buffer
Segment
Notes: Figure 3.9

## Slide 55: Layout of a TCP Segment
Bits | 0 15 |  |  | 16 31
0-31 | Source Port |  |  | Destination Port
32-63 | Sequence Number |  |  | 
64-95 | Acknowledgement Number |  |  | 
96-127 | Data Offset | Not Used | Flags | Receive Window
128-159 | Checksum |  |  | Urgent Pointer
160-191 | Options (Optional) |  |  | 
160+ 192+, 224+, etc. | Data |  |  | 
Notes: Figure 3.10

## Slide 56: TCP is Bi-Directional
Even if, logically, data only flows one way, in order to ensure reliability, we need return data which tells us which data has been successfully received (ACK)
The sender must maintain the buffered data until it receives an ACK

## Slide 57
Transport
Data
Header
Send Buffer
Receive Buffer
Byte Expected
Received Data
Sent Data
Start Byte
Start Byte + MSS
Sequence Number = Start Byte
Acknowledgement Number = Byte Expected
Unsent Data
Notes: Figure 3.11

## Slide 58
Header
Sequence Number = M
Transport
Send Buffer
Acknow-ledged
Last Acknowledged
= M
Next Sequence Number
= N
Unsent
To Send
Data
Transport
Receive Buffer
Received
Expected
= N
Just Received
Transport
Send Buffer
Acknowledged
Last Acknowledged
= N
Unsent
Header
Acknowledgement Number = N
Notes: Figure 3.12

## Slide 59: TCP Reliability
How to detect if something has gone missing
  A timeout
  Returning an ACK repeatedly which indicates the buffer hasn’t grown

## Slide 60: Packet Resent on Duplicate ACK
Seq # = 100
Data
Host A
Host B
Seq # = 200
Data
Seq # = 300
Data
Ack # = 200
Data
Ack # = 200
Data
Seq # = 200
Data
Ack # = 400
Data
Notes: Figure 3.15

## Slide 61: Packet Resent on Timeout
Seq # = 100
Data
Seq # = 200
Data
Ack # = 200
Data
Seq # = 200
Data
Timeout
Host A
Host B
Notes: Figure 3.16

## Slide 62: A Lost ACK Doesn’t Matter
Seq # = 100
Data
Seq # = 200
Data
Seq # = 300
Data
Ack # = 200
Data
Ack # = 400
Data
Ack # = 300
Data
Host A
Host B
Notes: Figure 3.17

## Slide 63: TCP Fairness
How does TCP decide when to send packets (with UDP you call “send”)?
It sends packets within increasing frequency but when they start going missing, it halves its rate
There are LOTS of variants of TCP
Protocols are often tested to see if there are TCP-fair, i.e. if N streams share a network link they get 1/N of the bandwidth
UDP protocols are often NOT TCP-fair, you need to add that functionality yourself

## Slide 64
Time
Rate (bytes/s)
10K
20K
30K
Notes: Figure 3.22

## Slide 65: Observations
If there is lots of data to send TCP can fill up IP packets, UDP might waste network capacity
There are potentially lots of ACK packets in TCP
TCP is slow to start, UDP is rapid start
UDP protocols need to play fair when there is congestion

## Slide 66: NETWORK LAYER

## Slide 67: Network Layer
The Internet is a collection of machines that understand IP packets
A network routes packets from one host to another through routers
Router
Route
Table
IP Packet
IP Packet

## Slide 68: IPv4
In IPv4 addresses are 32 bits in the form 128.16.13.118
They are running out and IPv6 is ready to be deployed

## Slide 69: IP Packets
Key problem is what happens if links support frames of different size
  E.G. Ethernet is 1500bytes
The solution is that IP supports packet fragmentation, where a large packet is broken in to smaller ones: the end point must then reassemble them
Obviously try to pick a maximum transmission unit (MTU) that avoids this

## Slide 70: IP Packet Format
Bits | 0 15 |  |  |  |  | 16 31 | 
0-31 | Version |  | Header Length |  | Type of Service | Total Length | 
32-63 | Identification |  |  |  |  | Flags | Fragment Offset
64-95 | Time to Live |  |  |  | Protocol | Header Checksum | 
96-127 | Data Offset | Not Used |  | Flags |  | Receive Window | 
128-159 | Source Address |  |  |  |  |  | 
 | Destination Address |  |  |  |  |  | 
160-191 | Options (Optional) |  |  |  |  |  | 
Bits | 0 15 |  |  | 16 31 | 
0-31 | Version | Header Length | Type of Service | Total Length | 
32-63 | Identification |  |  | Flags | Fragment Offset
64-95 | Time to Live |  | Protocol | Header Checksum | 
96-127 | Source Address |  |  |  | 
128-159 | Destination Address |  |  |  | 
160-191 | Options (Optional) |  |  |  | 
160+ 192+, 224+, etc. | Data |  |  |  | 
Notes: Figure 3.24

## Slide 71: Protocol Types
This is necessary to tell the receiver what the IP packet contains. E.G.s
  1: Internet Control Message Protocol (ICMP)
  2: Internet Group Management Protocol (IGMP)
  6: Transmission Control Protocol (TCP)
  17: User Datagram Protocol (UDP)
  89: Open Shortest Path First (OSPF)

## Slide 72: LINK AND PHYSICAL LAYER

## Slide 73: Link and Physical Layer
The one we all have experience with is Ethernet, either wired or wireless
Our experience is that for a specific Ethernet interface, we either need to:
  Set IP address manually
  Get an address automatically using DHCP
DHCP is actually an application-layer protocol
In both cases, we are making a mapping between the MAC address of the Ethernet adapter and the IP address

## Slide 74
Notes: Figure 3.31

## Slide 75
Bits | 0 15 |  |  |  |  | 16 31 | 
0-31 | Version |  | Header Length |  | Type of Service | Total Length | 
32-63 | Identification |  |  |  |  | Flags | Fragment Offset
64-95 | Time to Live |  |  |  | Protocol | Header Checksum | 
96-127 | Data Offset | Not Used |  | Flags |  | Receive Window | 
Bits | 0 15 | 16 31
0-31 | Destination MAC Address … | 
32-63 | … Destination MAC Address | Source MAC Address …
64-95 | …Source MAC Address | 
96-127 | EtherType | Data
… | Data | 
… | CRC Checksum | 
Notes: Figure 3.33

## Slide 76: Basic Networking Strategies

## Slide 77: Architectures
Peer to Peer
Client/Server
Hybrid

## Slide 78: Consider Just Two Machines
What is the relationship between them?
Peers?
Master/slave? Client/server?
Does one have data the other one does not?

## Slide 79: Peer to Peer with Two Clients
Need to decide separation of responsibilities
  E.G. Each client simulates one player’s actions
Need to communicate sufficient information to the other that they can get both get the same state
Assumes that they have the same information other than real-time input
Can be achieved simply with sending input to each other

## Slide 80: For Example DOOM
Doom ClientA
Read
Input
Rendering
Receive
Input
Simulate
Doom ClientC
Read
Input
Rendering
Receive
Input
Simulate
Notes: Figure 11.6

## Slide 81: Master Slave with Two Clients
One process calculates results of input
Necessary if simulation is non-deterministic

## Slide 82: For Example
Slave
Read
Input
Rendering
Master
Read
Input
Rendering
Receive
Input
Simulate
Notes: Figure 11.6

## Slide 83: More Clients
The same issues exist:
  Who is responsible?
  Who has the necessary data to evolve the state?
  Who can be trusted to evolve the state?

## Slide 84: Peer to Peer Architecture
Client
Client
Client
Client
Client

## Slide 85: Client-Server Architecture
Server
Client
Client
Client
Client

## Slide 86: Implications
Peer to Peer
  Data need to be sent multiple times on the network links might vary in bandwidth & latency
  Clients need to manage multiple connections
Client Server
  The Server is a bottleneck
  Clients manage one connection
  Server can have privileged data, and can probably be trusted
  Latency is higher
  Synchronization is easy

## Slide 87: Hybrid Architectures
Multiple servers serving different regions
Multiple service types & service layers
Server pool

## Slide 88: Which Protocol to Use?
If there is an application layer protocol that is appropriate use that!
UDP
  Good for fast changing data, and initial start update
  Good for position information
TCP
  Good for reliable data, and bulk data transfer
  Good for data assets and critical information such as score

## Slide 89: Which Protocol to Use?
Some people implement “reliability-lite” on top of UDP
Other platforms mix UDP & TCP
  There are many catches with this
Many platforms support application layer protocols such as HTTP or FTP for bulk asset transfer

## Slide 90: Summary

## Slide 91
NVEs & NGs have a long history, but it is in the last 10 years that they have really taken off
The Internet is a best effort network where applications need to deal with latency & loss
There are various architectures that support NVEs & NGs
In Part 2 we will look in detail at NVEs and NGs requirements, and compare this to what we actually get from the Internet today